## Slide 1: SOC FINAL - UART FIFO
第14組
111061560 吳俊鋌
111061534 陳白翀

## Slide 2: Outline
BLOCK DIAGRAM
FIRMWARE
UART.C OPTIMIZATION
Minimum FIFO DEPTH
CPU time
Total time
Quality of result
*baud rate 9600

## Slide 3: BLOCK DIAGRAM
RX FIFO
TX FIFO

## Slide 4: FIRMWARE
Interrupt is trigger ones the RX FIFO is full.
CPU starts to read out data from RX FIFO and than write it into TX FIFO.

## Slide 5: UART.C OPTIMIZATION
CPU read out reg_uart_stat twice if using following code :

## Slide 6: UART.C OPTIMIZATION
Using a integer to store reg_uart_stat can reduce 1089 cycles.

## Slide 7: FIFO DEPTH
RX FIFO can receive next data after RX FIFO is empty.
Since RX FIFO & TX_FIFO has same depth and the time of CPU read/write is a lot faster than UART.
Depth of TX FIFO can be less than RX FIFO.
5
4
3
2
1
0
CPU
5
4
3
2
1
CPU
5
4
3
2
1
CPU
5
4
3
2
1
0

## Slide 8: FIFO DEPTH
Improve from previous design, we let UART receive data while RX FIFO is not full.
UART can also receive/transmit data while CPU is read/write data.
So the whole system can transmit X data while the FIFO DEPTH is less than X.
5
4
3
2
1
0
CPU
6
5
4
3
2
1
CPU
7
6
5
4
3
2
CPU
5
4
3
2
1
0

## Slide 9: FIFO DEPTH
After interrupt, CPU read/write 10 data while UART finish transmit 1 data, so the FIFO DEPTH can be 9 while it can actually transmit 10 data.
Transmit 20(1~20) data with only 2 Interrupt & 9 length FIFO.

## Slide 10
Baseline :
  CPU time : ISR time + read/write time = 25284 cycles per data
Our work :
  CPU time : ISR time + read/write time*10 = 60020 cycles = 6002 cycles per data.
  (four times improve)

## Slide 11
Baseline :
  UART time : ISR time + Transmission time = 68753 cycles per data
Our work :
  UART time : ISR time + Transmission time*10 = 422918 cycles = 42291 cycles per data.
ISR time
Transmission time
ISR time
Transmission time

## Slide 12: Quality of result
baud rate 9600
Message length: 512
Baseline :
Latency = (68753*512*25)/1000 = 880038.4 us
Metric = 880038.4 us – 512*(1/9600) = 826705.066 us
Our work :
Latency = (42291*512*25)/1000 = 541324.8 us
Metric = 541324.8 us - 512*(1/9600) = 487991.466 us

## Slide 13: Q&A
Q: Explain the detail of FIFO working mechanism

## Slide 14: END